## Slide 1: Image Processing to Manipulate RGB Values Using Verilog
Presenter: Po-Yu Huang
UID:117684681

## Slide 2: Paper Demonstrate
Implementing the image processing in the Verilog code. This paper have showed how they converted an image in a hex file using MATLAB and then used the hex file in Verilog coding to perform some image processing operations.
Inversion operations: RGB - 255
Brightness operations: RGB + value
Threshold operations: if (RGB > Threshold): RGB = 255
Figure from paper:
https://www.irjet.net/archives/V5/i5/IRJET-V5I5341.pdf

## Slide 3: Constrains and difficulties
Verilog can’t read image directly much change to hexadecimal form. (bmp -> hex)
2. This paper is designed to simulate the code to simulate on virtual board environment. For this project, the virtual simulation is on VIRTEX 6 FPGA board. They run the simulation on Xilinx ISE. It used to simulate on Xilinx ISE, trying to simulating it on Xilinx Vivado.
Figure from Xilinx:
https://www.xilinx.com/products/boards-and-kits/ek-v6-ml605-g.html#specifications

## Slide 4: Part 1
Changing bitmap to hexadecimal. This part is written in MATLAB.

## Slide 5: Part 2: Image Processing
Defining the inputs that need to operate the image processing.

## Slide 6
Process and transmit 2 pixels in parallel to make the process faster, you can modify to transmit 1 pixels or more if needed
Notes: VSYNC: vertical synchronizing pulse
HSYNC: horizontal synchronizing pulse
This purpose is to create a Verilog model of am image sensor or camera in the case that you want to test your image processing algorithm, with your real-time image or video processing

## Slide 8: Brightness addition and subtraction

## Slide 9: Invert Operation

## Slide 10: Threshold Operation

## Slide 11: Part 3: Write out the image
Notes: This pulse is high it means that the data is valid.

## Slide 12: BMP format
The file header (14 bytes) contains information about file size and location at which data is stored.
The Image header (40 bytes*) tells information about rows and columns of an image, bits per pixel, type of compression used if any

## Slide 15: What else can I do?
Edge detection? Sobel, Canny